Tachometer wiring for GM/MSD coil modification

1991 Miata

# Text boxes

470 ohm

Red

Black

Green

Orange

# Loc: CAS harness

CAS signal

## White

# Loc: Tachometer harness

To drive tachometer

## Yellow/Blue

MOSFET IRF510

N-Channel  FET

Radio Shack p/n:

276-2072

# Loc: Igniter harness

+12V hot in run or start

## Blue

# Loc: Dedicated ground wire from PPF

Ground

## Black

Gate

Drain

Source